CD-ROM BOOKLET

GLOBAL MONTHLY AVHRR CLIMATOLOGY OVER LAND:

Clear-sky top-of-the-atmosphere variables

Garik Gutman,  Dan Tarpley,  Aleksandr Ignatov,

Satellite Research Laboratory, NOAA/NESDIS, Washington, D.C.

Steve Olson

Research and Data Systems Corporation, Greenbelt, MD

1. INTRODUCTION

These CD-ROMs contain a global 5-year  top-of-the-atmosphere (TOA)  clear-sky monthly climatology over land produced from  the Advanced Very High Resolution Radiometer (AVHRR).  This was  done within the Global Vegetation Index (GVI) project in the Satellite Research  Laboratory of the Office of Research and  Applications, National  Environmental  Satellite Data and  Information  Service (NESDIS), National Oceanic and Atmospheric Administration (NOAA). The  GVI  project was sponsored by the NOAA  Climate  and  Global Change Program for the purpose of developing improved operational GVI products that are useful for global climate studies.

The  data on these CD-ROMs are the third generation  GVI  D-level products described in the GVI User's Guide (Kidwell,  1994) and  Gutman et al. (1995), the latter included on this  CD.   The products are given at 0.15o resolution in a rectangular latitude/ longitude  (equal angle) projection.  They include  5-year  means and  standard deviations for each month of visible (0.63 µm)  and near-infrared  (0.85 µm) reflectances (@1, @2),  normalized  difference  vegetation index (NDVI=(@2-@1)/(@1+@2)), thermal  IR  (11 and  12 µm) brightness temperatures (T4, T5), precipitable  water index (PWI=T4-T5), and observational solar zenith angle.

A number of auxiliary files are included to facilitate data analysis.  The satellite based files are the Quality Description (QD) files, an Auxiliary Mask (AM) file, and a 10'-resolution remapped version of NDVI.  The non-satellite datasets contain soil and vegetation maps, topography, precipitation, etc. (see the content for details).

The QD files are monthly and include 5-year averages of the number of cloud-free observations (weeks), the biases of satellite scan angle, and the snow masks based on the visible reflectance and 11 µm temperature data.  The AM files are stationary (independent of the month) and contain land/sea tag, political boundaries and two surface type masks based on maximum (Vmax) and minimum (Vmin) annual NDVI values characterizing low annual variability in NDVI (Vmax-Vmin<0.2) for evergreen (Vmax>0.45) and deserts (Vmax<0.2).  Descriptions of the QD and AM files are given in Appendix 1.

The data processing is briefly described below.  Its full description  is given in Gutman et al. (1995) and is provided  on this CD-ROM in the directory  "/document/avhrrcli".  Programs  to read the data on several platforms are provided in Appendix 2.

2. BRIEF DATA PROCESSING DESCRIPTION

The processing comprises three stages: B (weekly), C (monthly), and D (climatology) (see Gutman et al. 1995 for the nomenclature and data products generation).

The processing of weekly data (B3.0/W15 _ B3.2/W15) was based on the GVI weekly composite raw data (counts) -- the second generation of GVI.  The processing steps included: 1) conversion of counts in AVHRR thermal channels to T4 and T5 and correction for calibration non-linearity; 2) calculation of reflectances in the solar channels, @1 and @2, using the updated (Pathfinder) calibration, which accounted for sensor degradation, correction for Sun-Earth distance and normalization to overhead sun; 3) cloud/clear identification using T4-thresholds dependent upon month, region, and viewing angle.  The NDVI=(@2-@1)/(@2+@1) and PWI=(T4-T5) were calculated at the B-level to retain accuracy.  All B-product values were packed into 8 bits.  Note that no atmospheric or angular corrections were applied to these data, hence no surface geophysical variables have been derived.  This is yet to be done (see details in Gutman et al. 1995).

The monthly processing (B3.2/W15 _ C3.2/M15) flow included the following steps: 1) QC flags were applied on a weekly basis, resulting in data gaps, 2) each quantity was averaged over one month (five weekly composites) for each map cell to partially fill in the data gaps and reduce some of the angular variability (the weeks that spill over into the next month were used for both the current and the previous months); 3) bi-linear spatial interpolation was applied to the missing data areas with persistent cloudiness in monthly averaged images; 4) 3x3 map cell running average smoothing was done to partially account for the imperfection of cloud screening, to filter out atmospheric and angular variabilities, and to compensate for different number of observations used in monthly averaging and for random spatial sampling from the original Global Area Coverage (GAC) data into the GVI map cells.  The monthly time series (C3.2/M15) of all the aforementioned variables for each individual year of the period from April 1985 - September 1994 are available at NOAA National Climatic Data Center (NCDC; e-mail: satorder@ncdc.noaa.gov).

The 5-year TOA AVHRR climatology (D3.2/M15) on this CD has been developed from the C3.2/M15 monthly fields of TOA @1, @2, NDVI, T4, T5, and PWI using data from April 1985 to December 1987 (NOAA-9), and from January 1989 to March 1991 (NOAA-11).

3. DISC ORGANIZATION, CONTENT, NAMING CONVENTIONS

There are two volumes to this set of CD-ROMs.

Volume  1  contains  the core climatologies  and  some  ancillary vector  overlay  data,  documentation for these  data,  and  some ancillary software tools.

Volume 2 contains selected regriddings of the core climatologies, designed to register with the National Geophysical Data  Center's Global  Change Data Base.  In addition, data from that data  base are  included.  Scientists wishing to perform  integrated  global environmental  studies  may find these ancillary  data  valuable.  Documentation  for the ancillary data is also included in  Volume 2.

The  CD-ROMs  have three directories discussed  below.   The directory structure of each CD-ROM is given in the root directory the respective CD-ROM.

3.1 Directory "data"

This directory contains has five main subdirectories:

"average", "qualflag", "standev", "ncillary", and "vector".

The  subdirectories "average" and "standev" contain  respectively the 5-year monthly means and standard deviations of  AVHRR reflectances (@1 and @2) and temperatures (T4 and T5),  Normalized Difference  Vegetation  Index (NDVI),  Precipitable  Water  Index (PWI), sensor scan angle (sca), and the solar zenith angle (sza).  The 8-bit files can be converted to floating point values using:

Conversion					Naming convention

@1(i) = 45.0 * (i) / 255.0 + 5.0		ch1

@2(i) = 35.0 * (i) / 255.0 + 15.0		ch2

T4(i) = 76.0 * (i) / 255.0 + 250.0		ch4

T5(i) = 76.0 * (i) / 255.0 + 250.0		ch5

ndvi(i) = 0.8 * (i) / 255.0 - 0.1		ndvi

pwi(i) = 7.0 * (i) / 255.0 - 2.0		pwi

sca(i) = 110.0 * (i) / 255.0 - 55		sca

sza(i) = 50.0 * (i) / 255.0 + 20.0		sza

s1(i)  = 4.0 * (i) / 255.0 			ch1

s2(i)  = 4.0 * (i) / 255.0			ch2

s4(i)  = 3.0 * (i) / 255.0			ch4

s5(i)  = 3.0 * (i) / 255.0			ch5

sndvi(i) = 0.1 * (i) / 255.0			ndvi

spwi(i)  = 0.5 * (i) / 255.0			pwi

ssca(i)  = 26.0 * (i) / 255.0			sca

ssza(i)  = 8.0 * (i) / 255.0			sza

where i is a count value from 0 to 255.

The  "qualflag"  directory  contains  12  monthly  QD  files monqd.img, where "mon" is as above. The "qualflag" directory also contains an auxiliary mask (AM) file maskam.img which represents

fields that do not change with month (see Appendix 1 for details).

The abovementioned subdirectories are in Volume 1.

The subdirectory "ncillary" contains global raster data sets on  soils, vegetation, etc. from the Global  Ecosystems  Database and TerrainBase produced by NGDC.  This directory is in Volume 2.

The  subdirectory  "vector" contains ancillary  vector  data (coastlines,  national  boundaries,  etc.) in  GRASS  and  IDRISI format.  This directory is in Volume 1.

3.2 Directory "document"

This directory contains the documentation for the data.  Its subdirectories describe all the databases used to assemble this CD-ROM.  A description of the contents for each subdirectory can  be found  in the file aareadme.1st in the root directory.   Portions of  this  directory are on Volumes 1 and 2, describing  the  data residing on those two CD-ROMs, respectively.

3.3 Directory "software"

This  directory contains three subdirectories:   "freeform", "geovu", and "html".

The  directory "freeform" contains FreeForm utilities, which  the user may find useful for format conversion and documentation  for several  types  of  data.   Documentation  is  available  in  the \geovu\freeform\document  directory.   Current  documentation  is updated  regularly at the Website of NOAA's National  Geophysical Data      Center.        Currently,     that      website      is http://www.ngdc.noaa.gov/seg/freeform/freeform.html.

The  directory  "geovu" contains GeoVu browse  and  visualization software, which has been adapted for use on these CD-ROMs.  GeoVu is provided for PCs, Macintoshes, and for Sun and Silicon  Graphics  UNIX workstations.  Documentation and sample data  are  also provided.   Under the GeoVu directory for each hardware  platform (for  example,  PC), there are installation  instructions.   Make sure that the gut_gvi1.men, gut_gvi2.men, and avhrrcli.lst  files are  copied from the CD to the directory you create on your  computer for running GeoVu.  For example, if you create a  directory called  c:\geovu on your PC to contain GeoVu software,  and  your CD-ROM is drive e, enter the commands:

copy e:\software\geovu\pc\gut_gvi1.men c:\geovu

copy e:\software\geovu\pc\gut_gvi2.men c:\geovu

copy e:\software\geovu\pc\avhrrcli.lst c:\geovu

to copy the files from the CD to your GeoVu software directory on your computer.

The geovu package is a general data access tool developed by NGDC to display grids and images, display and plot tabular data  sets, and  examine  related  documentation during  the  data  selection process.

The  directory "html" contains much of the "plastic  Website"  on the  CD-ROMs.  You may ignore this directory, unless you want  to "sleuth" the design of the CD.

3.4 Naming conventions

For the averages and standard deviations the naming convention is: varmon.img, where "var" is the variable, defined above (var=ch1, ch2, ...; e.g., pwi is the precipitable water index), and "mon" is the first three letters of the month (e.g., mon=jan, feb, ...)

ACKNOWLEDGMENTS

The GVI project has been supported by the NOAA Climate and Global Change Program.  Without its continuous funding, the generation of the 5-year global AVHRR climatology over land would not have been possible.  Critical reviewing by the NOAA program manager Dr. A. Gruber motivated this work.   are acknowledged for the development of the processing and visualization system.  Contributions in the project by J. Powers (NOAA/NESDIS), M. Halpert and C. Ropelewski (NOAA Climate Prediction Center), and P. Schultz, R. Hucek and L. Rukhovetz, D. Sullivan of Research Data Systems Corporation (RDC) are acknowledged.  This work was accomplished when one of the authors (A.I.) held National Research Council Associateship at the Satellite Research Laboratory, NOAA/NESDIS, on leave  from  the Marine Hydrophysics Institute,  Sevastopol,  Ukraine.   David Hastings of the National Geophysical  Data  Center managed the adaptation of these data to CD-ROM; David Schoolcraft assisted in the adaptation.

The requested form of acknowledgment for use of the data on this CD-ROM is as follows:

Gutman, G., D. Tarpley, A. Ignatov, and S. Olson, 1995:  Global Monthly AVHRR climatology over land: Clear-sky top-of-the-atmosphere variables.  Ed. D. Hastings. United States Dept. of Commerce, National Oceanic and Atmospheric Administration, National Environmental Satellite, Data, and Information Service, National Geophysical Data Center, Boulder, Co 80303, USA.

References

Gutman, G., D. Tarpley, A. Ignatov, and S. Olson, 1995:  The enhanced NOAA Global Land Dataset from the Advanced Very High Resolution Radiometer. Bulletin of the American Meteorological Society, 76, 1141-1156,

Kidwell, K., 1994: Global Vegetation Index User's Guide. U.S. Dept. of Commerce, National Oceanic and Atmospheric Administration, National Environmental Satellite, Data, and Information Service, National Climatic Data Center, Satellite Data Services Division, 126 pp.

Fig. 1: The organizational structure of CD-ROM.

APPENDIX 1

QUALITY DESCRIPTION (QD) FILES

The 8-bit QD files were generated for each month to describe some of the inherent statistical characteristics.  Each of the 8 bits is a 5-year average of the corresponding bit for each month of each individual year.  The following table describes how each bit was assigned:

BIT NUMBER	CRITERIA/COMMENT			BIT VALUE

----------	----------------			---------

1			nobs = 0 or 1 (mostly cloudy)		1, else 0

2			nobs = 2 or 3 (moderately cloudy)	1, else 0

3			nobs = 4 or 5 (mostly clear)		1, else 0

4			|sca| < 20 deg (near nadir)		1, else 0

5			sca > 20 deg (forward scatter bias) 1, else 0

6			sca < -20 (back scatter bias)		1, else 0

7			T4 < 270K and @1>20% (stable snow)	1, else 0

8			270K=T4=280K and @1> 20% 		1, else 0

(unstable snow)

where "nobs" is number of clear observations (weekly composites after cloud screening) per month per pixel.

AUXILIARY MASKS (AM) FILE

An  8-bit  AM  file  was  generated  for  delineating  land, political  boundaries,  and masking two surface  types  with  low annual   variability:  evergreen  vegetation  and   desert.   The following table describes each bit:

BIT NUMBER	CRITERIA/COMMENT					BIT VALUE

----------	----------------					---------

1		land location (no coast used)			 1, else 0 	2		state borders,inland water			 1, else 0

3		evergreen (Vmax-Vmin<0.2 and Vmax>0.45)   1, else 0 	4		desert (Vmax-Vmin<0.2 and Vmax<0.2)		 1, else 0

5		blank

6		blank

7		blank

8		blank

where Vmax and Vmin are annual maximum and minimum NDVI,respectively.

APPENDIX 2

READING THIRD GENERATION GVI IMAGES

I.   INTRODUCTION

This CD-ROM contains global Top-of-the Atmosphere (TOA)

images and products derived from Advanced Very High Resolution

Radiometer (AVHRR).  These products were developed on a Silicon

Graphics Inc. (SGI) workstation using the C language as part of

the Global Vegetation Index (GVI) project by the Climate Research

and Applications Division (CRAD) Land Surface Team of the Office

of Research and Applications (ORA).  The data on this CD-ROM

consists of D-Level products, which are described in

the GVI Users Guide (Kidwell, 1994).  In order to ensure easy

portability across all platforms, the data was scaled to 8-bits

or 1-byte.  Each uncompressed image is made up

of 2500 columns and 904 rows of data, with 0.144 degrees

(nominally 0.15 degrees) latitude/longitude resolution, giving a

total size of 2260000 bytes/image. The purpose of

this section is to read the 2500 x 904 image.

Each image is read by rows, starting with row 1 at 75 N, and

ending with row 904 at 55 S.  Every row begins at 180 W

longitude, and each successive map cell would be 0.144 degrees

east of the previous map cell.  Therefore, the upper left corner

of the image starts at 75 N, 180 W, and ends in the lower right

corner of the image, at 55 S, 180 E.  The physical range of the

data is between 0 and 255, with all ocean values containing the

value 0.

Since the binary imagery is character data, you cannot

browse through it.  However, the character data can be easily

converted into integer values.  The following is a list of

FORTRAN and C programs that can be used as a guide for reading

the files.  Each of these programs will convert the character

data into integer values.  Reading the 8-bit imagery is somewhat

platform specific.  The coding is broken down by language and

platform.

NOTE:   THE OUTPUT DATA IS BEING WRITTEN TO UNIT=6, THE SCREEN.

II.  USING FORTRAN

The following is a list of programs that should be used

based on your platform.

A.    Silicon Graphics (SGI), SUN Workstations, VAX AND DEC

ALPHA WORKSTATIONS

One word of caution with the VAX and DEC ALPHA.  Please make

sure that the data read from the CD-ROM or whatever media type

you are using blocks the data in 2500 byte blocks.  Particularly

with the VAX and DEC ALPHA machines, there is a tendency to

default to 512 byte blocks, which means you will NOT be able to

read the data with these programs.

To mount the CD-ROM on a VAX or DEC ALPHA machine, use the

following as an example:

mount devicename /media=cd /und=fixed:none:2500)

PROGRAM CONVRT

C

C    THIS PROGRAM IS DESIGNED TO READ 8-BIT IMAGE DATA AND

C    OUTPUT THE DATA AS ASCII TEXT WITH 2260000 RECORDS.  THIS

C    WORKS OUT TO 1 RECORD PER PIXEL.  UNIT 10 IS THE INPUT FILE

C    YOU ARE TRYING TO READ, AND IN THE EXAMPLE, UNIT 6 IS WHERE

C    THE OUTPUT IS GOING TO.

C

C **********************************************************

C   COMMENTS ABOUT THE FORTRAN READING PROGRAM

C **********************************************************

C

C   THE NUMBER OF COLUMNS IS 2500 AND THE NUMBER OF ROWS IS 904.

C   THE BLOCKING FACTOR IS 2500 BYTES.  YOU'LL NOTICE THAT THE

C   RECL (RECORD LENGTH) IS 625.  625 REPRESENTS THE NUMBER OF 4-

C   BYTE WORDS PER RECORD.  THE DATA WILL BE OUTPUT TO UNIT=6 ONE

C   PIXEL AT A TIME.  THEREFORE, THE OUTPUT FILE WILL CONTAIN

C   2260000 LINES OR RECORDS IN IT.  THE DATA STARTS IN THE UPPER

C   LEFT HAND CORNER AT 75N, 180W AND ENDS IN THE BOTTOM RIGHT

C   HAND CORNER AT 55S, 180E.  EVERY ROW BEGINS AT 180 W

C   LONGITUDE, AND EACH SUCCESSIVE MAP CELL IS 0.144x EAST OF THE

C   PREVIOUS CELL.  THE OUTPUT DATA RANGE WILL BE BETWEEN 0 AND

C   255.  THE OCEAN MAP CELLS ARE ALL ZEROS.

C

C **************************

C     DECLARE ALL VARIABLES

C **************************

C

CHARACTER*1 IMAGE(2500)

CHARACTER*8 HEX(2500)

INTEGER DATA(2500)

C

C ********************************

C         OPEN FILES TO READ

C ********************************

C

OPEN(UNIT=10,FILE='GVI.DATA',ACCESS='DIRECT',

$RECL=625,FORM='UNFORMATTED',STATUS='UNKNOWN')

DO 10 I=1,904

READ(10,REC=I) IMAGE

DO 15 J=1,2500

WRITE(HEX(J),'(Z2)') IMAGE(J)

READ(HEX(J),'(Z2)') DATA(J)

15        CONTINUE

DO 20 J=1,2500

WRITE(6,'(I4)') DATA(J)

20        CONTINUE

10      CONTINUE

STOP

END

*****************************************************************

B.    IBM MAINFRAMES

PROGRAM CONVRT

C

C    THIS PROGRAM IS DESIGNED TO READ 8-BIT IMAGE DATA AND

C    OUTPUT THE DATA AS ASCII TEXT.

C

C **********************************************************

C   COMMENTS ABOUT THE FORTRAN READING PROGRAM

C **********************************************************

C

C   THE NUMBER OF COLUMNS IS 2500 AND THE NUMBER OF ROWS IS 904.

C   THE BLOCKING FACTOR IS 2500 BYTES.  THE DATA WILL BE OUTPUT

C   TO UNIT=6 ONE PIXEL AT A TIME.  THEREFORE, THE OUTPUT FILE

C   WILL CONTAIN 2260000 LINES OR RECORDS IN IT.  THE DATA STARTS

C   IN THE UPPER LEFT HAND CORNER AT 75N, 180W AND ENDS IN THE

C   BOTTOM RIGHT HAND CORNER AT 55S, 180E.  EVERY ROW BEGINS AT

C   180 W LONGITUDE, AND EACH SUCCESSIVE MAP CELL IS 0.144x EAST

C   OF THE PREVIOUS CELL.  THE OUTPUT DATA RANGE WILL BE BETWEEN

C   0 AND 255.  THE OCEAN MAP CELLS ARE ALL ZEROS.

C ********************************

C    DECLARE ALL VARIABLES

C ********************************

C

CHARACTER*1 IMAGE(2500)

INTEGER*2 DATA(2500)

EQUIVALENCE(IMAGE,DATA)

C

C********   OPEN FILES TO READ   ********************************

C

OPEN(UNIT=10,FILE='GVI.DATA')

DO 10 I=1,904

READ(10,'(125(20A1))') IMAGE

DO 20 J=1,2500

WRITE(6,'(I4)') data(J)

20       CONTINUE

10    CONTINUE

STOP

END

*****************************************************************

C.    CRAY

With the CRAY, the following script (cray.sh) should be used

used with the compiled FORTRAN code.

PROGRAM CONVRT

C

C    THIS PROGRAM IS DESIGNED TO READ 8-BIT IMAGE DATA AND

C    OUTPUT THE DATA AS ASCII TEXT.

C

C **********************************************************

C   COMMENTS ABOUT THE FORTRAN READING PROGRAM

C **********************************************************

C

C   THE NUMBER OF COLUMNS IS 2500 AND THE NUMBER OF ROWS IS 904.

C   THE BLOCKING FACTOR IS 2500 BYTES.  YOU'LL NOTICE THAT THE

C   RECL (RECORD LENGTH) IS 625.  625 REPRESENTS THE NUMBER OF 4-

C   BYTE WORDS PER RECORD.  THE DATA WILL BE OUTPUT TO UNIT=6 ONE

C   PIXEL AT A TIME.  THEREFORE, THE OUTPUT FILE WILL CONTAIN

C   2260000 LINES OR RECORDS IN IT.  THE DATA STARTS IN THE UPPER

C   LEFT HAND CORNER AT 75N, 180W AND ENDS IN THE BOTTOM RIGHT

C   HAND CORNER AT 55S, 180E.  EVERY ROW BEGINS AT 180 W

C   LONGITUDE, AND EACH SUCCESSIVE MAP CELL IS 0.144x EAST OF THE

C   PREVIOUS CELL.  THE OUTPUT DATA RANGE WILL BE BETWEEN 0 AND

C   255.  THE OCEAN MAP CELLS ARE ALL ZEROS.

C

C ********************************

C    DECLARE ALL VARIABLES

C ********************************

C

CHARACTER IMAGE

C

C

Do J = 1,904

Do I = 1 , 2500

1          READ(10) IMAGE

write(6,*) ichar(IMAGE)

enddo

enddo

STOP

END

The shell script to use with the FORTRAN code is the

following:

#!/bin/sh

assign -R

assign -a gvi.data -sunblocked u:10

cf77 filename

./a.out

exit

where,

assign -R  =  Reset all assign attributes.

assign -a filename -sunblocked u:10  =  data file "filename" has

structure unblocked and has been assigned to unit 10.

cf77 filename = Use the cray FORTRAN 77 compiler on input file

"filename" containing program CONVRT code.

./a.out  = The executable

****************************************************************

III. USING C Language

The following program can be universally used on all

platforms which have a C compiler.

#include <stdio.h>

#include <math.h>

#include <stdlib.h>

/*

The purpose of this program is to read 1-byte plate carree

images (C-level or D-level) and output them as ascii text one

byte at a time.  One word of caution, if you are using a VAX

DEC ALPHA machine, then you need to make sure that the data

has been stored in 2500 byte blocks, NOT 512 byte blocks.

*/

static FILE *fp1, *fp2;

void main(int argc, char *argv[])

{

char image[2260000];

int xsize=2500, ysize=904;

register int i;

short data;

if (argc != 3)

{

printf("usage -- image_read inputfile outputfile\n");

exit(EXIT_FAILURE);

}

if (!(fp1=fopen(argv[1],"rb")))

{

printf("Cannot open file %s to read\n",argv[1]);

exit(EXIT_FAILURE);

}

if (!(fp2=fopen(argv[2],"w")))

{

printf("Cannot open file %s to write\n",argv[2]);

exit(EXIT_FAILURE);

}

fread(&image[0],1,xsize*ysize,fp1);

for(i=0;i<2260000;i++)

{

data=(short) image[i];

fprintf(fp2,"%d\n",data);

}

/*  Write output to user-defined file  */

}

To compile the program, use the following command:

cc read_image.c -o read_image

Then to run the program, use the following:

read_image inputfile outputfile

where,

read_image = The executable

inputfile =  The input 8-bit binary image

outputfile =  The output ASCII image

The output ASCII image will be a sequential file, with each pixel

constituting a new record.  Therefore, the entire image will have

2260000 records/lines.