README.DOC FILE
           DOCUMENTATION FOR DISSEMINATION OF NOAA/NOS
                 GRIDDED EEZ BATHYMETRIC DATA
                         JANUARY  1991

INTRODUCTION

This readme file accompanies digital bathymetric data, for a single
map area, collected as part of the National Oceanic and Atmospheric
Administration (NOAA) / National Ocean Service (NOS) program to map
the U.S. Exclusive Economic Zone (EEZ).

Data for this program are collected with multibeam swath sounding
techniques from areas close to land, where depths are about 100 to
150 meters, seaward to the limits of the EEZ which extends from the
coastline for 200 nautical miles.  For maps with areas having
depths shallower than 100 to 150 meters, standard NOS hydrographic
data supplement the EEZ multibeam data.

Each map area measures 1/2 degree of latitude by 1 degree of
longitude for all parts of the EEZ with the exception of the EEZ
surrounding Alaska.  Maps in Alaska's EEZ measure 1/2 degree of
latitude by 1 1/2 degrees of longitude.  Exceptions to this general
scheme may be made, especially where the map area is close to land
or close to the line defining the EEZ limits.

When NOAA ships conduct multibeam operations,  tracklines are
generally run parallel or subparallel to known contour lines.  The
swath of each trackline is perpendicular to the ship and overlaps
the swaths of adjacent, parallel tracklines by at least 10%, thus
ensuring complete coverage of the seafloor. The length of the
swath, measured along the seafloor, depends on water depth and the
type of multibeam system used. For NOAA's deep water multibeam
system (used in depths greater than 600 to 1000 meters) this length
is about 70% of water depth.  For shallow water systems, the swath
length is up to 250%.

DISK FILES AND DOCUMENTATION

The files on the CD-ROM, in the subdirectories

    \TOPO\NOSEEZ\<ocean area>\<data set>

are described below. Each data set subdirectory in the ocean areas
(ATLANTIC, PACIFIC, GOMEX, etc.) contains four data and description
files:

(1) a file containing a Universal Transverse Mercator (UTM) grid of
bathymetric sounding data (the .DAT file), with coordinates based
on meters, covering the map area. The grid spacing is 250 meters;
(2) a parameter file (the .PRU file) containing data needed to
interpret the UTM grid; (3) a second, more generalized, geographic
grid file (the .GRD file), with coordinates based on latitude and
longitude, covering the same map area.  The grid spacing is 15
seconds of latitude and longitude ; and (4) a second parameter file
(the .PRG file) containing data needed to interpret the geographic
grid.

Any data sets found to deviate from the information in this file
are accompanied by their own "README.DOC" file -- please refer to
that file for information about different grid sizes or other
anomalies.

In this readme file, hard copy (paper) documentation is replaced
by ".TIF" files of the figures, in addition to this text.  Two of the
figures show the data organization for the two types of grids.  The
third figure shows how the geographic grid is derived from the UTM
grid.  The figures are denoted "FIG_1.TIF", etc.  Any graphic program
capable of displaying the standard "TIFF" format may be used.
Macintosh users, please run the file "ABOUT_NOSEEZ" for a self-
displaying version of this file with the figures included.

THE BATHYMETRIC DATA IN THESE GRID FILES ARE NOT TO BE USED FOR
NAVIGATION.

NOS PROCESSING OF EEZ DATA 

The number of "raw soundings" or "full resolution data", resulting
from surveying a map area, typically total about 5 to 10 million. 
For each sounding there is a depth value, latitude, and longitude.
Positioning and sounding accuracy meet NOS and International
Hydrographic Organization standards.  Positional accuracy of
individual soundings is better than a 50 meter circular error of
position.  All depths have been corrected for the velocity of sound
in water and are judged to be well within one percent of the actual 
depths.  In the future, the full-resolution data will be made
available to the public from NOAA's National Geophysical Data
Center, Boulder, Colorado.

Selected soundings, chosen from the "raw soundings", typically
number about 300,000 for a map area.  They form the input to a
contouring program on a minicomputer. This software calculates the
depth values at the grid points of the 250 meter UTM grid.  The
details of the data processing are given by Herlihy and others
(1988).  The UTM grid is transferred from the minicomputer to a PC
where it is converted to a less dense geographic grid (covering the
same area as the UTM grid).

The UTM grid file (.DAT file) and the corresponding geographic grid
file (.GRD file) consist of a string of negative integer numbers.
Each number represents a depth, rounded to the nearest whole meter,
at a grid point.  It is important to note that, explicitly, there
are no X and Y UTM coordinates associated with these depths in the
UTM .DAT file and there are no latitude and longitude coordinates
given for depths in the geographic .GRD file.  These coordinates
are determined from the location of the grid point in the file and
from data contained in the two parameter files.

THE UTM GRID

This grid file (the .DAT file) is based on UTM coordinates and
contains soundings at grid nodes separated by 250 meters in both
the X and Y directions.  See Figure 1.  The X and Y coordinates of
all UTM grid points are in meters given in even multiples of 250.
The number of rows and columns in a UTM grid varies but it
generally has about 230 rows and a number of columns that is
dependent on latitude.  For example, at 27 degrees (the approximate
middle of the Gulf of Mexico EEZ) the number of columns is about
400 and at 44 degrees (off central Oregon) the number is about 330.
The total number of depth values (grid points) is rows * columns.
(* means multiplication). For most of the EEZ adjacent to the
conterminous United States, the number of grid points in a UTM grid
will vary from about 75,000 to 95,000.

Since the UTM grid is skewed relative to the map limits (i.e.,
relative to the north-south and east-west directions), and the grid
is defined so that the entire map will fall within it, this often
results in "indeterminate" grid points (points for which there are
no values)  along the four grid edges.  Also, for land areas (and,
in many cases, areas immediately adjacent to land) that fall within
the map limits, there are no depth values for the grid points.  The
method of indicating such indeterminate points in the grid file is
to place values of -32767 at the grid nodes.

The 250 meter grid was developed to produce contours for a series
of standard EEZ bathymetric maps corresponding to map areas as we
have defined them here.  All contours shown on these EEZ maps have
been made with the same UTM grid supplied on this disk.  These
multicolored maps are on a UTM projection, made at a scale of
1:100,000, and have a contour interval of 20 meters.  When one of
these maps is published, the corresponding gridded data are made
available to the public.

THE GEOGRAPHIC GRID

The geographic grid (Figure 2) is derived from the UTM grid and is
based on latitude and longitude.  It has sounding nodes (grid
points) every 15 seconds (1/4 minute) of latitude and longitude. 
For a single map area this results in exactly 121 rows and 241
columns giving it 29,161 grid points, about one third the number
of points in a typical UTM grid.  The grid spacing for the
geographic grid is about 463 meters in a north-south direction and
is variable in the east-west direction, depending on latitude.  At
27 degrees the east-west separation is about 412 meters.  The
method of deriving the geographic grid from the UTM grid is
graphically shown and explained in the caption of Figure 3. In this
grid there are no indeterminate points along the four edges, as in
the case of the UTM grid.  Missing data are indicated by zeros. 
In all cases these zeros represent land or areas adjacent to land. 

The geographic grid was developed for use on a PC.  There are two
reasons for making this grid rather than simply using the UTM grid
on a PC:  (1) the entire UTM grid, for one map area, is too large
to fit into most of the commercially available PC software used for
making graphical displays (this problem is solved by using the much
smaller geographic grid), and (2) the geographic grid, using this
same PC software, allows the two horizontal axes, for both contour
maps and three dimensional plots, to be labeled with latitude and
longitude.

PARAMETER FILES

There are two small parameter files, one for each of the grid
files.  The .PRU parameter file contains data for the UTM grid. 
The .PRG parameter file contains data for the geographic grid.
Some of the data contained in these files are needed to determine
grid point coordinates (see examples given below).  Other data are
for information only.  The numerical data are right justified and
contained in columns 2 through 16.  All text starts in column 18. 

COORDINATE DETERMINATION OF GRID POINTS

This section describes the methods of obtaining coordinates from
the UTM grid file and the geographic grid file.  The coordinates
from the UTM file will result in X and Y values in meters.  The
coordinates from the geographic grid file will result in latitude
and longitude values in decimal degrees.  It is important to
remember that these grid files differ, not only in the fact that
they have different kinds of coordinates, but also that the
arrangement of the rows and columns is not the same.  This
different ordering of rows and columns is clearly shown in Figures
1 and 2.  In both cases, when determining the coordinates of a grid
point, data from the appropriate parameter file, along with the
grid row and column, are required.

The UTM GRID

To determine the X and Y coordinates of a grid point in a UTM grid,
use the following equations:

     X = XMIN + (J - 1) * 250
     Y = YMAX - (I - 1) * 250

where I and J are the row and column numbers, respectively, of the
grid point as shown in Figure 1.  XMIN and YMAX are values taken
from the .PRU parameter file.  
To determine the I and J grid coordinates, specify the location of
the grid point number, NUM, in the grid file.  Also specify the
number of rows, IROW (taken from the parameter file), for the grid.
First a value J' is determined by evaluating the following
expression and truncating it to an integer: NUM / IROW - 0.0001. 

Then,

     J = J' + 1
     I = NUM - (J' * IROW).

As an example of this procedure, the row, I, and the column, J, of
the 2,297th point (NUM) in a grid file will be determined.  (This
is an example taken from the Monterey Canyon Map and the results
obtained do not apply to the data on this disk unless, of course,
this disk is for the Monterey Canyon Map).   From the .PRU
parameter file for the Monterey Canyon map, the following values
are obtained: IROW = 229; XMIN = 499750; YMAX = 4096000.  The
expression (NUM / IROW - 0.0001) is 10.0305.  The resulting values
are:

     J' = 10
     J = J' + 1 = 11
     I = NUM - (J' * IROW) = 7

Using the two equations given above, the following UTM coordinates
are determined:

     X = XMIN + (J - 1) * 250 =  502250 meters
     Y = YMAX - (I - 1) * 250 = 4094500 meters

These coordinates, along with the UTM zone number and the
horizontal datum used to process the data (both contained in the
.PRU parameter file), will allow latitude and longitude values to
be calculated with the appropriate software (see "Obtaining
Additional Information" at the end of this readme file).

The Geographic Grid

Here the method for deriving latitude and longitude for grid points
in the geographic grid is given.  The coordinates will be in
decimal degrees.  Note that west longitude is negative.

LATITUDE  = MINIMUM LATITUDE  + (I - 1) * FACTOR
LONGITUDE = MINIMUM LONGITUDE + (J - 1) * FACTOR

where FACTOR = 15 / 60 / 60 = 0.0041666667

To obtain the I and J grid point location within the grid (see
Figure 2), the following procedure (different than the one used
with the UTM grid) is used.

    I' is an integer from the truncated expression (NUM / JCOL - 
        0.0001)
    I = I' + 1
    J = NUM - (I' * JCOL)

where NUM, as before, is the numerical position of the grid point
within the string of grid point depth numbers and, in the case of
the geographic grid, JCOL always equals 241.

If the .PRG parameter file gives a minimum latitude equal to 26.5
degrees and a minimum longitude equal to -92.0 degrees (this
example is for the Orca Basin Map in the Gulf of Mexico) and the
coordinates of the 26,789th grid point (NUM) are desired, the
following row (I) and column (J) of the grid are obtained:

     I' = truncated integer of (26789 / 241 - 0.0001) = 111
     I = I' + 1 = 112
     J = NUM - (I' * JCOL) = 26789 - (111 * 241) = 38

Using the above equations, the following coordinates, in decimal
degrees, are obtained:

LATITUDE =   26.5 + (112 - 1) * (15 / 60 / 60) =  26.962500 degrees
LONGITUDE = -92.0 + (38 -  1) * (15 / 60 / 60) = -91.845833 degrees

OBTAINING ADDITIONAL INFORMATION

To obtain catalogues and current information about the availability
and pricing of NOAA's EEZ products (e.g., published multicolored
maps), contact:

     Distribution Branch, N/CG33
     National Ocean Service
     Riverdale, MD 20737-1199
     (301) 436-6990
     
For information about NOAA's EEZ unpublished, preliminary "blueprint"
(one-color) maps and other questions about the EEZ multibeam data,
contact

     National Geophysical Data Center
     NOAA Code E/GC3
     325 Broadway
     Boulder, CO 80303-3328
     (303) 497-6338
     InterNet:  info@mail.ngdc.noaa.gov

To obtain information about the geodetic programs and products
(including software to transform UTM coordinates to latitude and
longitude) supplied by the National Geodetic Survey, contact:

     National Geodetic Information Branch
     N/CG 174, Rockwall Building, Room 24
     National Geodetic Survey / NOAA
     Rockville, MD 20852
     (301) 443-8631

Note: The Maryland addresses were about to be revised in April, 1993.
For the latest information, contact NGDC, Boulder.


REFERENCES

Herlihy, D.R., S.P. Matula, and C. Andreasen (1988) Swath Mapping
Data Management Within the National Oceanic and Atmospheric
Administration, International Hydrographic Review, Monaco, LXV (2).